## Slide 1: Next generation of Solar PV Technologies Economic and environmental impact
Alessandro Martulli,1 Neethi Rajagopalan,2,3 Fabrizio Gota,4 Ulrich Wilhelm Paetzold,4 Toby Meyer,5 Cesar Omar Ramirez Quiroz,6,7 Robert Malina,1 Bart Vermang,1,8 Sebastien Lizin,1
1 Hasselt University, Belgium
2 VITO, Belgium
3 DOW, Belgium
4 Karlsruhe Institute of Technology, Germany
5 Solaronix, Switzerland
6 FOM Technologies, Denmark
7 NICE Solar Energy, Germany
8 IMEC, Belgium

## Slide 2: Background: Solar PV techs and supply chain
Silicon SJ (95% of market) | Thin-film SJ | Tandem (novel)
PERC | CIGS | Perovskite/CI(G)S
SHJ | CdTe | Perovskite/PERC
 | Perovskite (novel) | Perovskite/SHJ
Silicon: dominant Solar PV technology
China: dominant of silicon PV supply chain
IEA (2022)

## Slide 3: China’s dominance: Pros and Cons
PROS
About 90% solar cost decline
Solar = most affordabable source of electricity
CONS
Market concentration
  One technology, a few companies producing it
Geographic concentration (China)
China current energy mix reliant on coal
  Higher GHG emissions PV industry

## Slide 4: PV Supply chain diversification
Solar PV crucial technology to reduce energy GHG intensity
Supply chain diversification needed
Growing interest of EU and US policymakers to reduce dependence and stimulate domestic manufacturing
  Inflation Reduction Act (US)
  REPowerEU plan (EU)

## Slide 5: Alternative technologies
Silicon (95% of market) SJ | Thin-film SJ | Tandem (novel)
PERC | CIGS | Perovskite/CI(G)S
SHJ | CdTe | Perovskite/PERC
 | Perovskite (novel) | Perovskite/SHJ
Thin-film could be alternative to complement silicon supply
  Thin film tandems (perovskite/CI(G)S) show good performance (high-efficiency)
  Thin film equipment suppliers location: Europe/US
  Thin film R&D location: Europe/US
Can thin-film tandem PVs be competitive with silicon-based PVs (SJ and tandems)?
  Economic
  Environmental

## Slide 6: Research aim
Economic and environmental evaluation of PV technologies
  Silicon single-junction PVs: PERC and SHJ
  Thin-film single-junction PVs: Perovskite and CIGS
  Tandem PVs
    Perovskite/CIGS
    Perovskite/CIS
    Perovskite/PERC
    Perovskite/SHJ
Three geographical areas:
  Europe
  US
  China

## Slide 7: Economic and environmental indicators
Module-level: analysis until PV module production
System-level: deployment of PV modules in PV system to generate electricity
  Supported by Energy Yield calculations: annual energy generated at three climatic locations

## Slide 8: Results – USD$/W and kgCO2eq/W
Results include uncertainty on
  Material, Equipment prices
  Technical parameters (e.g., layer thickness, material utilization, energy consumption)
Chinese manufactured PVs have lowest price
EU manufactured PVs have lowest kgCO2eq/W
EU and US manufactured perovskite/CI(G)S
  Cost competitive with perovskite/silicon (China manufactured)
  Much lower carbon footprint if produced in EU
    35-47% reduction

## Slide 9: Results – Normalized environmental impact
Overall, environmental impact reduction compared to market available PERC
But, significant increasing mineral supply risk due to utilization of
  Indium
  Gallium
 | PERC | SHJ | CIGS | PVK | PVK/PERC | PVK/SHJ | PVK/CIGS | PVK/CIS
Global warming | 1 | 1.03 | 0.68 | 0.59 | 1.12 | 1.22 | 0.72 | 0.71
Ozone depletion | 1 | 0.87 | 0.35 | 0.27 | 0.74 | 0.68 | 0.41 | 0.40
Freshwater eutrophic. | 1 | 0.96 | 1.04 | 1.02 | 0.70 | 0.59 | 0.74 | 0.74
Marine eutrophication | 1 | 0.95 | 0.22 | 0.14 | 0.63 | 0.61 | 0.20 | 0.15
Freshwater ecotoxicity | 1 | 0.91 | 1.06 | 0.88 | 0.59 | 0.61 | 0.79 | 0.78
Terrestrial ecotoxicity | 1 | 1.02 | 0.89 | 0.46 | 0.91 | 0.78 | 0.80 | 0.79
Acidification | 1 | 0.97 | 0.66 | 0.55 | 0.80 | 0.81 | 0.71 | 0.69
Human toxicity | 1 | 0.95 | 1.07 | 1.06 | 0.58 | 0.57 | 0.75 | 0.74
Mineral scarcity | 1 | 1.12 | 2.67 | 0.61 | 0.98 | 1.04 | 2.21 | 1.78
Fossil scarcity | 1 | 0.96 | 0.62 | 0.57 | 0.72 | 0.71 | 0.57 | 0.56

## Slide 10: Results – LCOE and GEF
Results represent LCOE and GEF in EU, US and China
  PV module manufactured and installed in each region
Thin-film tandems are more cost competitive in areas and scales with higher system costs
  US (both scales)
  EU – residential
China has already very low system costs
   Tandem cost advantage is less evident
Thin film tandem GHG emissions advantage is significant for all scales and areas

## Slide 11: Results - Challenges
Stability is main concern for perovskite development and commercialization
Consider perovskite degradation influence on results
Traditional PV panels degradation ~ 0.40-0.50 %/year
Results: degradation under 0.70%/year for perovskite devices would be needed
Also here, thin-film competiveness shown
(results refer to PV modules installed in EU)

## Slide 12: Results - Challenges
Silicon techs, contrary to thin-film, can already rely on large-scale production
  Easier cost reductions in the next decades
How PV techs LCOE would change with:
  Increasing PV worldwide capacity
  Developing market share of PERC, SHJ and tandems
To remain LCOE competitve, thin-film tandem PVs would need:
  Higher device efficiency – at least 35%
  Further lower costs

## Slide 13: Conclusions
Market and geographic concentration: Chinese PV production of silicon-based PVs
Diversification might come from alternative technologies: thin-film tandems
LCOE comparison shows competiveness with traditional PVs, even if manufactured in the EU
Large carbon footprint reduction of Solar PV industry if manufacturing diversification is implemented
  US and Europe
Silicon large scale production would favor perovskite/silicon tandems. Some challenges would need to be overcome for thin-films:
  Further improve perovskite stability (in common with silicon-tandems)
  Consider Indium and Gallium utilization: scarce materials, more costly in the future?
  Further improve efficiency and/or reduce costs to maintain competitiveness in the next decades